In your class project system, you will need to grip 20mm glass vials and 20mm plastic vial caps. Since every team will need this, we will first design some gripper tooling for grasping those components. Pick a pneumatic gripper from the list below, and choose either the glass vial or the cap as your object. Now design two components for tooling. Component #1 is a bracket to attach to the pneumatic gripper, and the other is a soft jaw that will attach to your bracket.

Gripper choices:
1. SMC MHZ2-16D

2. SMC MHZ2-20D

3. SMC MHZ2-25D

4. Destaco Robohand RPLC-1

5. Destaco Robohand RPL-4M

6. Destaco Robohand DPDL-047M-038

7. Destaco Robohand DPDL-088

8. Destaco Robohand DTH-1M-L

Download or make a 3d model of your chosen gripper, and glass vial or cap, then design your hard and soft tooling parts, finishing with an assembly of all pieces to verify fit and clearances.

Grabcad or Partcommunity are good places to find models. For example, the SMC grippers can be found at: https://b2b.partcommunity.com/3d-cad-models/mhz2-parellel-style-air-gripper-standard-type-smc .

Upload to D2L dropbox:
1. Screenshot or pdf of assembly render with gripper, your tooling parts, and vial or cap.

2. STL file exports of your tooling parts, with files named: your_name_hard.stl and your_name_soft.stl for the two different parts (hard for the bracket that attaches to the gripper, and soft for the jaw that attaches to your bracket).