## Slide 1: Tank Controller PCB
By Jair Cordova
Notes: * Hello, everyone
* My name is Jair Cordova
* Today I will be presenting on a tank controller PCB Redesign for the open acidification project. The open acidification project is a set of projects, whose mission is to provide an inexpensive open-source set of tools to conduct ocean acidification research

## Slide 2: Background
What is Ocean Acidification?
What is Walla Walla University doing to help study this?
Notes: Ocean Acidification is when CO2 is released into the atmosphere and the oceans absorb part of it into its water, which lowers its pH. which can have many harmful effects
To combat this, an open-source research-grade device was created for less than $250.
  Unfortunately, the old design has parts like the two buck converters that have become unavailable, and the micro controller used is slower, more expensive, and has limited availability when compared to other options like the Raspberry Pi Pico 2 W
  To combat this problem, a new design was needed

## Slide 3: New Design
Notes: The new design has the Pi Pico 2 W at the heart of the design
it also has one 120V to 5V buck converter and a linear regulator to supply power to components
  These two components were used as we need both, 5V and 3.3V in the design
  5V is used for the two channel relay module
  3.3V is used on everything else
This new design also includes a BNC connector for the Temperature sensor instead of an 3.5 mm connection (audio jack)

## Slide 4
Notes: * Here is a full picture of my schematic:
Parts:
Pi Pico 2 W
Power Management
Sensors
Other Peripherals
Keypad
SD Card Component
Ethernet hat(no on schematic)

## Slide 5: Power Management
120 V to 5V Buck converter
Linear Regular
Relay
Notes: 702W-00_53 is the power receptacle with Earth, Neutral, and Line connections
This is then connected to the Buck converter which steps down 120V to 5V.
This 5V powers the relay module as well as the linear regulator which will regulate the voltage from 5V to 3.3V and power the rest of the components in the PCB.
It’s also important to note, the screw terminals up here connect the Earth and Neutral lines to the power outlet on the tank controller box and the hot line connector goes to the relay module which then connects to the outlets.

## Slide 6: Sensors
Temperature Circuit
pH Circuit
Protocol: I2C (share bus)
Notes: Here are sensors the board uses
This includes the temperature circuit which uses a module from atlas scientific. This module differs from the old design as the old board used an Adafruit module. This board is also now connected to a BNC connector as seen here
There is also a pH circuit that connects here and is the same module as was used in the old design
Both of these sensors communicate using I2C which allows them to share the bus as seen here

## Slide 7: Other Peripherals
Real Time Clock
Display
Protocol: I2C (share bus)
Notes: Other Peripherals
A Real time clock which is the same module used in the old design which uses the I2C protocol
As well as a display. This display used differs from the old design as the old display used too many pins. This new display uses the I2C protocol which uses less pins and allows it to share the bus with other devices. In this case the Real time clock.
The display is 16x2 chip on glass lcd module and has libraries available

## Slide 8: SD card
Protocol: SPI
Surface Mounted Component
Notes: Here is the SD card component and it’s connections. This part needed to be replaced as the old design used an Ethernet hat specific for the Arduino which had an SD card reader to it.
This component uses 10 k ohm pull up resistors on these 5 pins as stated in the official sd card standard.
For the power component of this, two capacitors in parallel and a series resistor have been added to keep the device safe. This is done as without it, when a card is plugged in and the device powers on, there will be an inrush of current which has been known to cause brownouts.

## Slide 9: Alternatives
Temperature Circuit
- Adafruit vs Atlas Scientific and BNC connector
5V or 3V Buck Converter
  - Relay
Raspberry Pi Pico Family
Notes: Some alternatives that were considered included:
  Using the Adafruit or atlas Scientific temperature circuits. Ultimately it was decided by the client who wanted to have the possibility to swap out this temperature circuit for other sensor circuits by atlas scientific. This is possible as other sensor circuits have the same pin outs and dimensions. Code will be needed to adapt this change.
I also considered using a 120 V to 3.3V buck converter to not need to use a linear regulator but no other relay modules were found from a trust worthy distributor that fit our specifications.
There was also debate on whether to use the Raspberry Pi Pico wireless version or not. The client decided it would be convenient to be able to use wireless as he wouldn’t have to route ethernet cables to every box. Unfortunately, this may not be an option for other universities or research facilities so an ethernet hat can also be mounted on top.

## Slide 10: Constraints and limitations
Physical Constraints
Monetary constraints
Component | Number | Cost per unit | Total cost
Raspberry Pi Pico 2 W | 1 | $7.00 | $7.00
Atlas Scientific EZO RTD Temperature Circuit | 1 | $35.99 | $35.99
Atlas Scientific Temperature Sensor | 1 | $23.99 | $23.99
Ethernet Hat | 1 | $4.95 | $4.95
SD Card | 1 | $0.13 | $0.13
LCD | 1 | $3.77 | $3.77
4x4 keyboard | 1 | $9.36 | $9.36
Atlas Scientific EZO pH circuit | 1 | $45.99 | $45.99
Atlas Scientific Electrically isolated carrier board | 1 | $41.99 | $41.99
Power Receptacle | 1 | $1.54 | $1.54
Power Outlet | 2 | $1.15 | $2.30
BNC Connector | 1 | $4.99 | $4.99
Buck Converter Module | 1 | $7.99 | $7.99
2 Channel Relay Module | 1 | $6.25 | $6.25
Real Time Clock | 1 | $6.95 | $6.95
Miscellaneous (ex. Resistor, Screws, etc.) | N/A | N/A | $26.04
Total |  |  | $229.23
Notes: * There have been any constraints and limitations in this project including physical and monetary constraints
* Physical constraints include limited number of pins
* and monetary constraints include keeping the PCB and it's components under $250

## Slide 11: Next Steps
PCB Layout
Fabrication
Testing

## Slide 12: Questions?
Notes: * how are you going to know that there isn't a bug in the design?
- physically check for short circuits
- prototype some test code with dr. james foster