## Slide 1: Tank Controller PCB
By Jair Cordova
Notes: * Hello, everyone
* My name is Jair Cordova
* Today I will be presenting on a tank controller PCB Redesign for the open acidification project. The open acidification project is a set of projects, whose mission it is to provide an inexpensive open-source set of tools to conduct ocean acidification research

## Slide 2: Background
What is Ocean Acidification?
What is Walla Walla University doing to help study this?
Notes: Ocean Acidification is when CO2 is released into the atmosphere and the oceans absorb part of it into its water, which lowers its pH. which can have many harmful effects
Sadly the barrier to enter this field is very high as devices to research this are very expensive
To combat this, an open-source device was created for less than $250 which monitors pH and temperature in an aquarium to study the effects of ocean acidification
  Unfortunately, the old design has parts like the two buck converters that steps down the incoming voltage have become unavailable, and the microcontroller used is slower, more expensive, and has limited availability when compared to other modern options
  To combat these problems, a new PCB design was needed

## Slide 3: New Design
Notes: The new PCB design has the Pi Pico 2 W at the heart of the design. This microcontroller was chosen for it’s easy of use as well as price point, upgraded specs, and availability on the market.
The New PCB design also has one 120V to 5V buck converter and a linear regulator to supply the correct power to components
  These two components were used as we need both, 5V and 3.3V in the design
  5V is used for the two channel relay module
  3.3V is used on everything else
This new design also includes a BNC connector for the Temperature sensor instead of an audio jack connector. This is because a temperature sensor with BNC connector can be bought off the self from companies like atlas scientific.
It’s also important to mention most of these parts are modules instead of standalone parts as one of the goals of this project was to make it easy for biologists to build with out strong technical knowledge in engineering.
The one exception to this goal was certain surface mounted components which are placed on the PCB during production

## Slide 4: Power Management
Power Receptacle
120 V to 5V Buck converter
Linear Regular
Screw Terminals
Relay
Notes: 702W-00_53 is the power receptacle with Earth, Neutral, and Line connections
This is then connected to the Buck converter which steps down 120V AC to 5V DC.
This 5V powers the relay module as well as the linear regulator which will regulate the voltage from 5V to 3.3V and power the rest of the components in the PCB.
It’s also important to note, the screw terminals up here connect the Earth and Neutral lines to the power outlet on the tank controller box and the hot line connector goes to the relay module which then connects to the outlets.
The old system used a more complicated system with two buck converters that had became unavailable.

## Slide 5: Sensors
Temperature Circuit (different)
pH Circuit (same)
Protocol: I2C (share bus)
Optional Extra Sensing Module
Notes: Here are sensors the board uses
This includes the temperature circuit which uses a module from atlas scientific. This module differs from the old design as the old board used an Adafruit module. This board is also now connected to a BNC connector as seen here
There is also a pH circuit that connects here and is the same module as was used in the old design
Both of these sensors communicate using I2C which allows them to share the bus as seen here. This differs from the previous PCB design as it used to communicate using UART
Another benefit of using I2C is that since the bus is shared, an extra sensing module can be optionally added for dissolved oxygen

## Slide 6: Other Peripherals
Real Time Clock (same)
Display (different)
Protocol: I2C (share bus)
Notes: Other Peripherals
A Real time clock which is the same module used in the old design which uses the I2C protocol
As well as a display. This display differs from the old design as the old display used too many pins. This new display uses the I2C protocol which uses less pins and allows it to share the bus with other devices. In this case the Real time clock.
The display is 16x2 chip on glass lcd module and has libraries available

## Slide 7: SD card
Surface Mounted Component (different)
Protocol: SPI
Notes: Here is the SD card component and it’s connections. This part needed to be replaced as the old design used an Ethernet hat specific for the Arduino which had an SD card reader to it.
This component uses 10 k ohm pull up resistors on these 5 pins as stated in the official sd card standard.
For the power component of this, two capacitors in parallel and a series resistor have been added to keep the device safe. This is done as without it, when a card is plugged in and the device powers on, there will be an inrush of current which has been known to cause brownouts.
This component is a surface mounted component which makes this PCB easier to assemble for the end user as the manufacturer solders it on during production which makes one less thing to worry about and is practically free.

## Slide 8
Notes:   Here is a 3D render of the PCB which was designed on KiCAD
  Mechanical constraints needed to be considered when designing the PCB, as certain parts needed to be on the edge. An example of this is are the BNC connectors as well as the button, Pi Pico, and power connector
  Other constraints include limited number of pins as well

## Slide 9
Notes:   Other constraints of this design include the number layers in the PCB.
  I ended up going with a 4-layer design, with the top and bottom layers being data planes and the middle being power and ground
  I also used vias for heat dissipation down here to act like a heat sink and spead the heat to the inner layers which were more solid
  IPC-2221A standard were followed here for the minimum spacing requirements between traces.
  One notable trace of this Tank Controller handles with approximate peak voltage of 170 V. This requires a minimum spacing for these traces of 3.2 mm. This clearance was added around traces in order to prevent creepage.

## Slide 10: Cost Analysis
Component | Number | Cost per Unit | Total Cost
Elegoo Arduino Mega clone | 1 | $17.49 | $17.49
KEYESTUDIO Ethernet shield | 1 | $18.99 | $18.99
Adafruit MAX31865 | 1 | $14.95 | $14.95
PT100 Temp Sensor (3-wire) | 1 | $12.98 | $12.98
1602 LCD | 1 | $4.25 | $4.25
4x4 Keypad | 1 | $1.50 | $1.50
2 Channel Relay Module | 1 | $6.79 | $6.79
Adafruit PCF8523 Real Time Clock | 1 | $4.95 | $4.95
Atlas Scientific EZO pH Circuit | 1 | $41.99 | $41.99
Atlas Scientific Electrically Isolated Carrier Board | 1 | $41.99 | $41.99
Power Receptacle | 1 | $1.46 | $1.46
Power Outlet | 2 | $1.15 | $2.30
3.5mm Jack Receptacle | 1 | $1.30 | $1.30
5V AC DC Buck Converter Module | 1 | $2.80 | $2.8
9V AC DC Buck Converter Module | 1 | $2.36 | $2.36
Miscellaneous (ex. Resistor, Screws, etc.) | N/A | N/A | $26.04
Total |  |  | $202.13
Component | Number | Cost per unit | Total cost
Raspberry Pi Pico 2 W | 1 | $7.00 | $7.00
Atlas Scientific EZO RTD Temperature Circuit | 1 | $35.99 | $35.99
Atlas Scientific Temperature Sensor | 1 | $23.99 | $23.99
Ethernet Hat | 1 | $4.95 | $4.95
SD Card | 1 | $0.13 | $0.13
LCD | 1 | $3.77 | $3.77
4x4 keyboard | 1 | $9.36 | $9.36
Atlas Scientific EZO pH circuit | 1 | $45.99 | $45.99
Atlas Scientific Electrically isolated carrier board | 1 | $41.99 | $41.99
Power Receptacle | 1 | $1.54 | $1.54
Power Outlet | 2 | $1.15 | $2.30
BNC Connector | 1 | $4.99 | $4.99
Buck Converter Module | 1 | $7.99 | $7.99
2 Channel Relay Module | 1 | $6.25 | $6.25
Real Time Clock | 1 | $6.95 | $6.95
Miscellaneous (ex. Resistor, Screws, etc.) | N/A | N/A | $26.04
Total |  |  | $229.23
Similar Price Tag
Additional price for boards
Notes: Monetary constraints include keeping the PCB and it's components under $250
The Table on the left shows the costs of the old PCB design while the table on the right shows the costs of the new PCB designs
As shown, the new design has a similar price tag as the old design as well as staying under out $250 goal
Additionally something that was not shown here is the cost to manufacture 5 boards from JLC PCB, which totaled to $108.61. This includes the merchandise total, shipping charge, customs and taxes, and sales tax.
5 boards were ordered to have backups in case for potential defects, and because the cost difference between a single board and a small quantity like 5 is often minimal due to fixed setup and manufacturing costs.
This brings the means the manufacoring costs of the PCB itself is around $20 which still under the $250 goal

## Slide 11: Testing
Overall Inspection of the Board
Continuity Tests
Correct Power Verification
Software Testing
Board Improvements Found
Notes:   Overall Inspection of the board included checking for physical damage and correct component placement.
  Next I did continuity tests to make sure the correct traces were connected together.
  After this I verified the correct power was being supplied to the components
  Finally, I worked on software testing, which involves running simple code to make sure parts are working. This includes the display, keypad, and sensors
  Certain things were found during testing that can be fixed on board revisions. This includes awkward placement of the Ethernet hat and incorrect display connection spacing.

## Slide 12: Future Work
New board Revisions
  Correct Display Cable
  Position the Ethernet Hat on one of the sides
Design Housing
Advance Software
Notes: *this leads me to my next point which is future work
Future work includes correcting the display cable to have the right spacing and positioning the ethernet on one of the sides
As well as Design Housing
Lastly, improving the software

## Slide 13: Summary
Design Criteria Followed
Improve accessibility to research-grade equipment
Understand the effects of ocean acidification
Notes:   The design criteria were followed which focused on pricing, functionality, ease of use, and device longevity.
  This will allow for this field to continue to grow as it will improve the accessibility to research-grade ocean acifidification equipment
  This intern should help us to understand the effects of ocean acidification better

## Slide 14: Questions?